## Slide 1: – QC Flags – A New Hope
David Simonin, Wojciech Smigaj and Chris Thomas

## Slide 2: Background and requirements
QC flag requirements
Flags for the DA:
  The DA algorithm just needs to know if an observation should be assimilated or not:
    A simple accept/reject flag will do. [R_1]
  [Optional] flag representing if an observation is ‘active’ or ‘passive’ [R_2]
Background
  UFO provides the observational operators needed to compute departures and innovations
  UFO must pre-process observations in order to select “good quality” observations.
  The observation quality need to be recorded  needed by DA algorithms and Monitoring
Flags for the Processing/Monitoring:
  Flags representing the processing step that has rejected an observation [R_3]
  Could be mutually exclusive and directly link to the simple accept/reject DA flag
  Diagnostic flags providing additional information (needed by monitoring system) [R_4]
  Independent of the accept/reject DA flag, not mutually exclusive, and user defined

## Slide 3: Proposal
namespace QCflags {
// Actual rejection flags
constexpr int pass = 0; // we like that one!
constexpr int missing = 10; // missing values prevent use of observation
constexpr int preQC = 11; // observation rejected by pre-processing
constexpr int bounds = 12; // observation value out of bounds
constexpr int domain = 13; // observation not within domain of use
constexpr int thinned = 16; // observation removed due to thinning
[…]
constexpr int onedvar = 25; // observation failed to converge in 1dvar check
constexpr int bayesianQC = 26; // observation failed due to Bayesian background check
constexpr int modelobthresh = 27; // observation failed modelob threshold check
constexpr int history = 28; // observation failed when compared with historical data
}; // namespace QCflags
Requirement [R_1]: accept/reject DA flag
  Use the existing QCflags: [R_1]  QCflags::pass
Requirement [R_3]: Flags representing the processing step
  Using existing QCflags categories to provide basic rejection information
Already in JEDI

## Slide 4: Proposal
New additions
Create a new Diagflags “mechanism” where flag definitions of key value pair (name/bit index) are provided via Yaml and can be completely user specific.
How to handle requirements [R_2] and [R_4]?
Diagnostic flags definition:
- unfolded: 1 # <flag name>: first unused bit index
- poisson thinning: 2 # <flag name>: first unused bit index
  By creating a new Yaml section
  By using a new filter
filter: Create Diagnostic Flags
flags:
- name: unfolded
initial value: true # optional; by default, false
bit index: 15 # optional; by default, the first unused bit index
As Diagflags are not mutually exclusive bit index are required when writing into file such as the ODB
The presence of the ‘passive’ Diagflags could be handled by the FinalCheck filter  Setting obs error to the largest float. (This may depend on the ‘passive’ definition and may not be valid for VarBC)

## Slide 5: Functionality
filter: Perform Action
where:
- variable:
name: IsDaytime@ObsFunction
is_in: 1
action:
name: set # set/unset of diagflags
flag: Daytime # Diagflags name
Using the Diagflags
  Only Diagflags
  Diagflags and QCflags
filter: ...
actions:
- name: reject # QCflag associated to this filter
- name: set # set/unset of diagflags
flag: Cloudy # Diagflags name
- name: set # set/unset of diagflags
flag: ReallyCloudy # Diagflags name

## Slide 6: Implementations
Option 1: Diagflags are stored in ObsSpace variables
  No need for a separate diagnostic flag manager
  All filters will automatically have access to the Diagflags values
  Each Diagflags will be represented by a std::vector<bool>
  Accessing and modifying values of Diagflags.
    Similar to any other member of the ObsSpace  calling the standard ObsSpace::get_db and put_db methods, which will gain new overloads taking a std::vector<bool> object.
    The put_db will have an additional input for handling bitIndex (stored as an attribute of the IODA variable).
For example, the flag indicating whether radialWind measurement has been unfolded would be stored in a variable called DiagnosticFlags/Unfolded/radialWind.
  How are diagnostic flags represented in NetCDF and ODB files.
    ODB: Transform all Diagflags groups into a bitfield using the key value-pair name/bitIndex provided in the Yaml.
    HDF5/NetCDF: Using bitfield or store each Diagflags in a separate array (using unsigned char type)

## Slide 7: Implementations
Option 2: Duplicate what is done for Qcflags
  Flags are managed by a new DiagflagsManager object storing a collection of ObsDataVector<bool> objects.
class DiagflagsManager {
public:
explicit DiagflagsManager(ObsSpace &obsspace);
void createFlag(const std::string &name, int bitIndex = -1, bool initialValue = false);
ObsDataVector<bool> & operator[](const std::string &name);
bool has(const std::string &name) const;
int bitIndex(const std::string &name) const;
void save(); // save flags to the ObsSpace.
private:
ObsSpace &obsspace_;
std::map<std::string, ioda::ObsDataVector<bool>> flags_;
std::map<std::string, int> bitIndices_;
};
This object needs to be passed to the constructor of each filter (OOPS will require some changes).
More consistent with current mechanism and possibly will yield better performance over option 1.

## Slide 8: Implementations
Option 2: Duplicate what is done for Qcflags
  Reading and updating diagnostic flags:
  Using the overloaded [] operator of DiagflagsManager
ObsDataVector<bool> &unfolded = Diagflags[“Unfolded”];
std::vector<bool> &unfoldedRadialWind = unfolded[“radialWind”];
for (size_t obsId = 0; obsId < unfoldedRadialWind.size(); ++obsId)
unfoldedRadialWind[obsId] = true;
  How are diagnostic flags represented in NetCDF and ODB files:
  Similar to option 1

## Slide 9: Thank you very much