## Slide 1
This work was performed under the auspices of the Significant Opportunities in Atmospheric Research and Science Program. SOARS is managed by the University Corporation for Atmospheric Research and is funded by the National Science Foundation, the National Oceanic and Atmospheric Administration, the Cooperative Institute for Research in Environmental Science, and by the Center for Multiscale Modeling of Atmospheric Processes.
Acknowledgments
Image Processing Algorithms for Aerosol Removal in Solar Coronal Images
Abstract
Coronal mass ejections, which are explosions of solar material and energy into space, pose a potential threat to satellite and electrical grid infrastructures, yet little is known about the solar corona. Various questions exist, relating to the origins of these mass ejections as well as the mechanisms involved in coronal heating. The corona and coronal mass ejections are measured by satellite and ground-based coronagraphs, instruments that produce a false eclipse of the Sun in order to separate the extremely faint coronal signature from the bright solar disk. The Earth’s atmosphere and the presence of aerosols limit the usefulness of images obtained from ground-based coronagraphs compared to satellite observations. We have developed image processing algorithms to remove aerosols from a new high-speed detector in real-time. We first generated two images from a time series of images containing real aerosols; a mean and a median image. We then applied a thresholding algorithm to all of the images within the time series. If the pixel values exceed the mean and/or median image value, they were replaced with the value in that mean or median image. Both techniques were successful in removing aerosols from imagery. Due to signal to noise advantages gained by utilizing the mean image instead of the median image, we feel that is the preferred method. Processing ~1s of imagery (150 fps) required ~180s on a dual-core 2.33 GHz CPU. Further optimization will promote real-time aerosol removal in solar observation.
Curtis L. Walker, State University of New York College at Oneonta, Oneonta, NY, 13820
Scott Sewell, High Altitude Observatory, National Center for Atmospheric Research, Boulder, CO, 80301
Steve Tomczyk, High Altitude Observatory, National Center for Atmospheric Research, Boulder, CO, 80301