## Slide 1
This work was performed under the auspices of the Significant Opportunities in Atmospheric Research and Science Program. SOARS is managed by the University Corporation for Atmospheric Research and is funded by the National Science Foundation, the National Oceanic and Atmospheric Administration, the Cooperative Institute for Research in Environmental Science, and by the Center for Multiscale Modeling of Atmospheric Processes.
Image Processing Algorithms to Remove Aerosols from Solar Coronal Images
Abstract
Coronal mass ejections, which are explosions of solar material and energy into space, pose a potential threat to satellite and electrical grid infrastructures, yet little is known about the solar corona. Various questions exist, relating to the origins of these mass ejections as well as the mechanisms involved in coronal heating. The corona and coronal mass ejections are measured by satellite and ground-based coronagraphs, instruments that produce a false eclipse of the Sun in order to separate the extremely faint coronal signature from the bright solar disk. Earth’s atmosphere and the presence of aerosols limit the usefulness of images obtained from ground-based coronagraphs compared to satellite observations. We have developed image processing algorithms to remove aerosols from a new high-speed detector in real time. Two images were first generated from a time series of images containing real aerosols; a mean and a median image. Then a thresholding algorithm was applied to all of the images within the time series. If the pixel values exceeded the mean and/or median image value, they were replaced with the value in that mean or median image. Both techniques were successful in removing aerosols from imagery. Due to signal-to-noise advantages gained by utilizing the mean image instead of the median image, the mean is the preferred method. Processing ~1 second of imagery (150 frames per second) required ~180 seconds on a dual-core 2.33 GHz CPU. Further optimization will promote real-time aerosol removal in solar observation.
Curtis L. Walker (1,2), Scott Sewell (3), Steve Tomczyk (3)
1: Significant Opportunities in Atmospheric Research and Science, University Corporation for Atmospheric Research,
2: State University of New York College at Oneonta, 3: High Altitude Observatory, National Center for Atmospheric Research
Methods
Figure 4: Single frame shows aerosols as white dots. The primary aerosol constituent this day was cottonwood pollen. The diagonal structure was the building’s edge, our occulting disk.
Figure 5: Aerosol trajectories over a time series of approximately 1 second. This image was obtained by taking the standard deviation of all 120 images in the time series.
Figure 6: Image histogram shows pixel brightness values measure in Analog-to-Digital Units (ADU). Peak at 500 ADU is due to building, peak at 200 ADU is due to blue sky.
Figure 7: Histogram spike at 4000 ADU due to aerosol contamination of image. Aerosols appear as white, or saturated, pixels.
Acknowledgments
Development of Time Series Based Algorithms to Remove Aerosols
From the data set, a mean and median image were calculated on a pixel-by-pixel basis. Each pixel element was evaluated 120 times and a mean/median value was calculated. All of these values were then recreated into a unique image that would serve as the basis for pixel replacement.
Figure 8: Mean Image
Figure 9: Median Image
Mean Time Series Algorithm
Median Time Series Algorithm
This algorithm utilized the mean image and analyzed our complete time series on an image-by-image basis comparing an individual image to this mean image. If a pixel was greater than two standard deviations above the mean value, it was replaced with the pixel element from the mean image.
This algorithm utilized the median image and analyzed our complete time series on an image-by-image basis comparing an individual image to this mean image. If a pixel was greater than two standard deviations above the mean value, it was replaced with the pixel element from the median image.
Figure 12: Image result from Median Time Series Algorithm. Aerosols were not present.
Figure 11: Image histogram shows similar structure to initial histogram.
Figure 10: Image result from Mean Time Series Algorithm. Aerosols were not present.
Figure 13: Image histogram shows similar structure to initial histogram.
Characteristics of Aerosol Distribution Time Series in Boulder, CO on June 16, 2010
Background
Corona is Sun’s “Atmosphere”
~10⁶ K plasma
Origin of the Solar Wind (constant energy radiation)
Coronal Mass Ejections (CMEs) can disrupt our satellite and electrical grid infrastructures as well as pose health risk to astronauts
Corona can only be seen naturally during total solar eclipse
Coronagraphs are instruments that produce a false solar eclipse via an occulting disk, and come in satellite and ground-based varieties
Figure 1: Total solar eclipse, July 11, 1991, observed at Hawaii.
Photo Credit: S. Koutcmy, IAP-CNRS (France)
Figure 2: Zeiss Coronagraph at Lomnicky Peak Observatory in Slovakia
Photo Credit: Steve Tomczyk
Obtain time series of 120 images as a data set to develop and evaluate algorithms to remove aerosols.
Calculate a mean and median image from the time series on a pixel-by-pixel basis. Each pixel is evaluated 120 times and a mean/median brightness value is calculated. The calculated mean/median brightness values were converted into an image.
Analyze each pixel in the time series to determine if its brightness value exceeded two standard deviations above the mean brightness value. Each pixel was evaluated 120 times to account for aerosol motion over the time series.
If no, leave alone.
If yes, replace that pixel with the same pixel element from mean/median image. Pixel replacement scheme using the mean/median image and a threshold of two standard deviations above the mean (2-sigma).
Contact: Curtis Walker, walkcl50@suny.oneonta.edu
Results
Conclusions & Future Work
The algorithms removed aerosols from the time series efficiently
Future evaluation will determine subtle deviations between the mean and median methods
Future work hopes to optimize these algorithms for real time performance (One second of data takes one second to process).
Time Series Acquisition
To create algorithms that would remove aerosols, a time series of images containing aerosols was obtained. A time series of 120 images was obtained in Boulder, CO on June 16, 2010 at 150 frames per second. This was accomplished by pointing the camera towards the sky, with the Sun obscured just behind the edge of a building like an occulting disk, and capturing the signal of aerosols illuminated by the Sun. This data set was analyzed visually and quantitatively prior to algorithm development.
Figure 3: This diagram shows the necessary setup to acquire the data set. The lines represent the camera’s field of view incorporating the aerosols and the building’s edge, but just missing the bright disk of the Sun.
Image Processing & Analysis
SUN
Building Edge
Table for computer and camera mount
Aerosols
Photon Focus CMOS Camera
Lens pointed towards sky using the building edge to obstruct sun (similar to occulting disk), but allow enough sunlight to illuminate aerosols.