## Slide 1: Image Processing Algorithms for Aerosol Removal in Solar Coronal Images
Curtis Walker – UCAR/SUNY Oneonta
Scott Sewell – NCAR/HAO
Steve Tomczyk – NCAR/HAO

## Slide 2: Solar Corona
Sun’s “Atmosphere”
~10⁶ K plasma
Origin of the Solar Wind
Emits massive quantities of energy
Can only be seen during total solar eclipse
May be viewed with coronagraphs outside of eclipse
Total solar eclipse, July 11, 1991, observed at Hawaii.
Photo Credit: S. Koutcmy, IAP-CNRS (France)

## Slide 3: Solar Coronagraph
Instrumentation that produces a false eclipse of the sun allowing coronal observation
Ground-based and satellite-based varieties
Zeiss Coronagraph at Lomnicky Peak Observatory in Slovakia
Photo Credit: Steve Tomczyk
LASCO Satellite
Photo Credit: NASA SOHO

## Slide 4: Image Processing
Dark Frame Corrections
Flat Field Corrections
Aerosol Removal

## Slide 5: What Do Aerosols Look Like?

## Slide 6: Measurement of Aerosol Motion
The white tracks represent aerosol trajectories over ~1s.
Final image processed of 120 images.

## Slide 7: How Do We Correct For Aerosols?
Three techniques for image thresholds
  Mean Threshold
  Median Threshold
  Minimum Threshold
A series of 120 images containing atmospheric aerosols were obtained in Boulder, CO on June 16, 2010 and were limited by the above thresholds.

## Slide 8: Quality of Aerosol Removal Using Mean Threshold
Mean threshold of all pixels in all 120 images. Note the aerosol streaks near the building and at left.
Final image processed of 120 images.

## Slide 9: Quality of Aerosol Removal Using Median Threshold
Final image processed of 120 images.
Median threshold of all pixels in all 120 images. Note that this is the best result.

## Slide 10: Conclusions & Future Work
We have successfully removed aerosols from an image utilizing the mean and median array thresholds
We will still attempt the minimum array threshold and other techniques for comparison